Radial platform Airfoil

The purpose of the proposed numerical methods project is to investigate the lift and drag curves of symmetric-elliptical airfoils that are swept in a circle about a centre axis. The proposed geometry is shown in Drawing 1 and Drawing 2; a simple elliptical airfoil is swept 360 degrees about an axis that is parallel to the normal lift vector while airflow will be modelled with a constant velocity along a cylindrical section inside the shape . The airflow is shown as arrows in the below pictures.

Drawing 1: Top View

Drawing 2: Symmetric View

An inviscid, incompressible, steady-state flow will be first simulated using Euler's equation. Viscous or friction effects will then be added along with compressible effects if time permits. The cylindrical co-ordinates of the Euler/Navier-Stokes equations (mass and momentum) will be discretized using known first-order or second order methods. When these equations are solved at steady-state, the integration over the airfoil will be numerically computer to calculated drag and lift. There are no readily available experimental or analytical solutions to this problem that can be compared with but a limiting case can be done as the radius approaches to infinity, the solution converges to the well-known 2D problem.

The end goal of these numerical simulations is to see if it possible to:
- create enough lift for flight
- reduce/eliminate induced drag
- have steady-state hovering